## Slide 1
Fatigue in Offshore Wind Monopiles
Comparison of S-N curves from various standards, new regression analyses, and parameters influencing the size effect in welds
Federico Della Santa, Ali Mehmanparast
These structures are subjected to cyclic loading (fatigue) and circumferential welds ;
The thicker the plate the lower the fatigue life;
Monopiles have to withstand a number of cycles greater than 10 million cycles (ultrahigh-cycle fatigue, UHCF).
Current issues
The size of the monopiles is increasing as a response to the required , up to:
  120 𝑚 length
  10 𝑚 diameter
  150 𝑚𝑚 wall thickness
Design standards are tailored for the high-cycle fatigue (HCF) due to experimental limitations;
Some studies suggest that the current S-N curves (thickness correction included) might be overconservative for monopiles
References: [1] Ruijuan Sun: “Reliability & Economic Evaluation of Offshore Wind Power DC Collection Systems”. [2] Strom-Forschung: “Reliable frequency converters for wind turbines”. [3] Andrew Kusiak: “Renewables: Share data on wind energy”. [4] Chen Zhang: “A survey on federated learning”. [5] Brendan McMahan: “Communication-Efficient Learning of Deep Networks from Decentralized Data”. [6] Le Trieu Phong: “Privacy-Preserving Deep Learning via Additively Homomorphic Encryption”.
Background by Schmidt Sergey, WEBTECHOPS LLP, Andrejs Kirma, Adrien Coquet, and Laymik from Noun Project
S-N curves comparison from three international standards
Designers check the fatigue life span of monopiles by looking at the S-N curves in the standards. The equation
Monopiles contain double V-groove butt welds that can be either:
In as welded conditions (AW):
  Presence of the weld toe
  Less expensive
  Shorter fatigue life due to stress concentration
Ground Flush (GF):
  Absence of the weld toe
  More expensive
  Longer fatigue life